## Slide 1
BORN MECHANICAL AND ID INTEGRATION 24TH JULY13

## Slide 2
6.2mm
11.8mm
13.5mm
8mm
USB COVER
SILICONE
BAND
RELEASE
CLIPS
METAL COVER
BAND
CLIP
DIMENSION OVERVIEW
5.4mm
32mm
11mm
3.8mm

## Slide 3
VIBRATOR
CURVED BATTERY
35MAH
BAND CLIP
MAIN CHASSIS
DIE CAST ALUMINIUM
LCD &
MICROSWITCH
USB PCB
SPRING CLIP
RIGD-FLEX PCB
BT ANTENNA
CHASSIS MODULE ASSEMBLY: OVERVIEW OF PARTS
BT CHIPSET

## Slide 4
MAIN BODY ASSEMBLY
USB PCB+RIGID-FLEX PCB SITS INSIDE THE MAIN CHASSIS (CONNECTED)
PCBA CONNECTS TO BATTERY, VIBRATOR AND MICROSWITCH/LED
CHASSIS MADE FROM MAG ALLOY AND HOLDS THE BAND CLIP IN PLACE
CUTOUT FOR BT ANTENNA IN THE MAIN CHASSIS
MAIN MODULE ASSEMBLY: FEATURES

## Slide 5
MAIN BODY ASSEMBLY + OVERMOULD
MAIN BODY ASSEMBLY OVERMOULDED IN SILICONE
USB PCB PROTRUDES OUT WITH THE GUIDE PROVIDED BY THE CHASSIS
COMPLETELY SEALED UNIT IS WATERPROOF
METAL COVER IS THEN PLACED OVER THE TOP – SEE NEXT PAGE
MAIN MODULE ASSEMBLY OVERVIEW
SILICONE OVERMOULD
USB IS COMPLETELY SEALED

## Slide 6
MAIN BODY ASSEMBLY + METAL COVER
PRESSED METAL COVER PLACED OVER THE TOP OF OVERMOULD
PRESSED COVER ALSO INTEGRATES THE BUTTON THAT ACTS AS A LIGHTGUIDE – SEE BELOW
MICRO SWITCH AND LED ARE SEALED BY THE SILICONE OVERMOULD
MICRO SWITCH UNDER THE
SILICONE OVERMOULD
MICRO SWITCH & LED
SECURED BY CHASSIS
LED SHINES THROUGH SEMI-
TRANSPARENT SILICONE &
THROUGH THE METAL COVER
FINAL MODULE ASSEMBLY OVERVIEW
THE METAL COVERS COULD BE CHANGED BY THE END USER TO DIFFERENT COLOURS AND ALSO FINISHES. IT ALSO PROVIDES A GOOD CHANCE FOR CUSTOM BRANDING OPPORTUNITIES

## Slide 7
BAND CLIP AS PER TAG
SPORT WATCH
CLOSED POSITIION
OPEN POSITIION
OPEN POSITIION
INTERFERENCE FLEXES THE SILICONE BAND & HOLDS IN PLACE
WHEN CLIP OPEN CLEARANCE ENABLES BAND TO GO IN.
BAND IS CUT TO SIZE
BAND CLIPPING OVERVIEW

## Slide 8
USB COVER HAS CLIP
THAT LOCKS INTO THE CHASSIS FRAME
USB COVER LOCKS ONTO THE METAL CHASSIS
BUTTON PUSHED DOWN ANDLOCKS INTO METAL CHASSIS
USB COVER & MAIN BODY OVERVIEW

## Slide 9
DIMPLE DETAILS ON INSIDE OF THE SILICONE BAND
SILICONE BAND IS CUT TO
REQUIRED SIZE. CUT
LINES ON THE BAND AND
CHASSIS HELP TO ALIGN
AND POSITION IN PLACE
BOTTOM SURFACE THAT
RESTS ON WRIST IS SILICONE
SILICONE BAND OVERVIEW

## Slide 10
HOLE IN THE METAL CHASSIS FOR THE BT ANTENNA
CLIP RELEASE MECHANISM INTEGRATED INTO THE USB COVER
DETAILS